## Slide 1: Smart Water Project
A TI-Innovator STEM Project
for the TI-84 Plus CE or the
TI-Nspire CX

## Slide 2: Overview of Tasks
1. Project Overview and Intro to Programming
Overview
2. Introduction to the TI-Innovator Hub
Introduction to Input/ Output
3. Mini Project: Using Input and Output
Using the On-Board Brightness Sensor
Problem
Supply List
Example of Completed Project
Task: “Hello World”
Task: Blink RGB LED
Write a program to Control Sound with Light
Task: Display Colors
4.Using External Input and Output Devices
Intro to external input and output devices
5. Putting it all together: Smart Water Project
Define the Problem
6. Presentation: Explain your product/design (optional)
Gallery Walk of Student designs and/or
Mini Project(s):
4.1: Light Sensor (external)
4.2: Digital Temperature and Humidity (DHT) Sensor
4.3: Soil Moisture Sensor
MOSFET Transistor and Pump set-up
Develop the Solution
Write the Code
Test and Debug
Team presentations of designs
Notes: This project is estimated to take 1.5-3 days depending on student’s familiarity with the technology and coding. There are areas that can be covered in detail, or less, depending on the time allotment.
This presentation is designed to be used in the classroom/camp to guide students through the tasks they can complete. This presentation by default is set-up for TI-84 Plus CE users, but also has hidden slides providing sample code for TI-Nspire CX users, as appropriate.

## Slide 3: 1. Project Overview

## Slide 4
Football and famine in Zimbabwe
Chidyamakondo high school, near Masvingo in southern Zimbabwe, has won the national girls’ football championships three years in a row. But that cherished record – and far, far more – is now at risk.
“Students are fainting, struggling to concentrate in lessons, dropping out of school … we’re having to shorten our assemblies and cut back on sport,” says head teacher Morrison Musorowegomo.
“Some of our players would rather leave the school and get married, or they will simply stay in the villages because they have no food.”
The Guardian,
April 21, 2016
Source: https://www.theguardian.com/global-development/2016/apr/21/drought-southern-africa-heavy-toll-students-fainting-malawi-zimbabwe

## Slide 5: More on Zimbabwe:
Notes: =

## Slide 6: Drought Conditions:
“South Africa, traditionally a regional breadbasket, is just recovering from what it described as its worst drought in about 30 years, receiving the lowest rainfall in 2015 since recording began in 1904.”

## Slide 7: Web resources for additional background on the drought in Zimbabwe and related issues :
Climate and Agriculture of Zimbabwe
http://www.our-africa.org/zimbabwe/climate-agriculture
Conservation Agriculture in Zimbabwe
http://www.fao.org/in-action/conservation-agriculture-contributes-to-zimbabwe-economic-recovery/en/
Capturing Rainwater in Cisterns
https://www.thestandard.co.zw/2017/01/15/zimbabweans-capture-rainwater-future-use/
Videos created by young people in Zimbabwe
http://www.our-africa.org/zimbabwe

## Slide 8: The Problem:
A drought in South Africa has caused a famine in Zimbabwe and local students are quitting school and soccer to stay home and help grow food for the family.
Read the full story for full background in The Guardian using the URL below.
  https://www.theguardian.com/global-development/2016/apr/21/drought-southern-africa-heavy-toll-students-fainting-malawi-zimbabwe
Notes: Discuss with students other “problems” that a smart-er watering system could be beneficial for:
For example, water restrictions are often put in place during the hot summer months in areas of excessively hot and dry climates. A smart water irrigation system could alleviate some of these restrictions as well, if people are smarter about the way they water their yards.

## Slide 9: The Design Challenge:
You are challenged to help solve the problem by designing and building a smart watering system to manage a limited amount of water collected in a cistern to irrigate a garden.
Notes: The project serves as a framework to teach concepts in algebra, ecology, computer programming, engineering
and global awareness.

## Slide 10: Engineering Design Process:
Define Problem
Design a proposed solution (Pseudocode)
Present group’s design to class.
Listen to feedback and make appropriate changes.
Build and test the design. – (Write the program)
Use test results to make appropriate and informed changes to design.
Present your solution to class.
Notes: It might be worth it to discuss with student that in very open ended where a single desired outcome that all of these steps would be important.

## Slide 11: Project Parts List:
TI-Nspire CX family or TI-84 CE Graphing Calculator
TI-Innovator Hub
4 AA Batteries and Battery Holder
Temperature & Humidity Sensor
Moisture Sensor
Light Sensor
MOSFET
Water Pump Motor DC 3V Mini Submersible Water Pump for Fountain Aquarium 120L/H Max Lift 3.6FT
2 male to male breadboard jumper cables (for 4 AA Batteries/Holder)
1/4” I.D. (Inner Dimension) x 3/8” O.D. Outer Dimension) tubing
Drinking straws
Duct Tape
1 Gallon milk jug
*Perlite or other medium for the plants to grow in
*Fast germinating seeds like radish, lettuce or similar.
* optional materials
Notes: This project works well with students working in groups of 3-4. Each student should ideally have their own calculator, all other materials are shared as a team. *Optional- If desired, the project can be continued over a longer period of time where the watering water system can be leveraged to grow an indoor garden.

## Slide 12: Project Parts List – Technology components
Input
Output

## Slide 13: Assembled Pump Example

## Slide 14: 1.2 Introduction to Programming
Optional- Review of Basic Programming Skills
Notes: This section is intended to provide a review of basic coding tips. It can be skipped if students are already familiar with basic programming on the calculator. The task in this section are in both the related Mood Ring, and Pet Car Alarm projects, so if students have completed either of those activities already, the tasks will be review.

## Slide 15
Important Keys on your TI 84 Plus Graphing Calculator
Dangerous
Use Del Instead of Clear
Store Key
Parentheses
Notes: Whenever we need to type out commands , use the green arrows above
Be sure to close your “ ” and ( )
Select commands from the prgm menus
Programs are automatically saved as you type
Some keys take you out of the Program Editor but you don’t lose your work.

## Slide 16: Background: Programming tips
To break out of a program press and hold the ON key until you receive a Quit option.
Do not forget to be very careful with the “Clear” button – you will lose the entire line of code typed.
Use the menus as much as possible. Do not try to type out the commands
TI-84
Quit Option that occurs when you break out of a program.

## Slide 17: Student Task: Create and execute a program to display “Hello World”
Write a program that displays a text message on the calculator using the Disp command.
Now, write the program to display the text message on the calculator 10 times using For command
Try a different type of loop
Example Code:
For(I,1,10)
Disp “Hello World”
End
TI-84
?
Notes: If student needs steps by steps support to write a basic program, reference TI Codes: 10 Minutes of Code : Unit 1 Skill builder 1.
Note that if the student has done the related Mood Ring or Pet Car Alarm project, this task will likely be review, and will test their recall of basic coding skills.

## Slide 18: Note to the Teacher- 10 Minutes of Code References for the Tasks
This project is not considered a “beginner’s” project.
If students struggle with the above basic task, and/or have little to no experience with coding prior to this project, it is strongly recommended that students should complete 10 Minutes of Code lessons and/or start with the related Mood Ring project before proceeding with this project.
Refer to the Teacher Notes PDF for additional information.
For your convenience, specific references to 10 Minutes of Code can be found in the notes section on each slide involving a task.
  10 Minute of Code Links:
  10 MOC for TI-84 Plus: https://education.ti.com/en/activities/ti-codes/84/10-minutes
  10 MOC for TI-Innovator for TI-84: https://education.ti.com/en/activities/ti-codes/84/10-minutes-innovator
  10 MOC for TI-Nspire CX: https://education.ti.com/en/activities/ti-codes/nspire/10-minutes
  10 MOC with TI-Innovator for TI-Nspire CX: https://education.ti.com/en/activities/ti-codes/nspire/10-minutes-innovator

## Slide 19: 2. Introduction to the tI-Innovator Hub
Notes: This section is intended to provide a review of coding with the TI-Innovator. It can be skipped if students are already familiar with basic programming on the calculator with the use of the TI-Innovator Hub. The tasks in this section are in both the related Mood Ring, and Pet Car Alarm projects, so if students have completed either of those activities already, the tasks will be review.

## Slide 20: Introduction: Input and Output
Input and Output occur in several forms.
  Input:
    User Inputs amount of red for RGB display
    Brightness sensor on TI-Innovator Hub measures light intensity
  Output:
    Calculator displays measured light intensity
    LED light displays color based on code

## Slide 21: Brightness Sensor on TI-Innovator Hub
INPUT
On-Board Light Brightness Sensor
OUTPUT
LED Light
Notes:   10 MOC for TI-Innovator for TI-84: https://education.ti.com/en/activities/ti-codes/84/10-minutes-innovator
  10 MOC with TI-Innovator for TI-Nspire CX: https://education.ti.com/en/activities/ti-codes/nspire/10-minutes-innovator

## Slide 22: Student Task: Write Program to Display Colors
Student Task: Write Program to Display Colors
  Create and execute a program using the COLOR command to display different colors using the Red-Green-Blue LED.
Example Code:
Send("SET COLOR 255 0 0”)
Wait 1
Send("SET COLOR 255 0 255”)
Wait 1
Send("SET COLOR 255 127 80”)
Wait 1
Send("SET COLOR 0 0 0”)
TI-84
?
Notes: This Task may be a review for students, if they completed the Mood Ring or Pet Car Alarm project prior to this one. If student needs steps by steps support reference : 10 Minutes of Code with the TI Innovator Hub : Unit 1/SB2
COLOR (Red Green Blue) Output LEDs (Built-in the TI-Innovator™)
The COLOR object built into the TI-Innovator includes 3 LED’s that can be set together or individually. The settings are from 0, off, to 255, full power.
Note that there are 256 (2^8) states for the setting. This is referred to as an 8-bit color setting
Command syntax: Send(“SET COLOR red green blue”)

## Slide 23: Exploration
What values would you enter to get blue?
What values to enter to get yellow?
Experiment with values to make your own colors
How can you make Red?
How can you make the other primary colors?
How can you make Yellow?
How can you make the other secondary colors?
How can you make White?
How can you turn off all of the colors?

## Slide 24: Extension
Student Task: Using a For loop, design a program that asks the user to enter a value for red, green and blue, the sent the color of the RGB LED on the TI-Innovator Hub that color for 2 seconds. Then turn the light off.
For(A,1,3)
Input ”ENTER RED VALUE, 0-255: ”,R
Input ”ENTER GREEN VALUE, 0-255: ”,G
Input ”ENTER BLUE VALUE, 0-255:”,B
Send("SET COLOR eval(R) eval(G) eval(B)”)
Wait 2
Send ("SET COLOR 0 0 0”)
End
TI-84
?
Notes: If student needs steps by steps support reference : 10 Minutes of Code with the TI Innovator Hub : Unit 2 Skill builder 1

## Slide 25: Student Task: Blink the RGB LED
Define Problem
  Explore turning on and off a flashlight. How does that work? How long does it stay on?
Develop the Solution
  Write down the steps before programming, For example:
      Step 1: Turn Light On
      Step 2: Wait 1 second
      Step 3: Turn Light Off
      Step 4: Wait 1 second
Write the code.
  Write the code. Make the RGB LED blink multiple times.
Notes: If student needs steps by steps support reference : 10 Minutes of Code with the TI Innovator Hub : Unit 2 Skill builder 2
Students are introduced a template for planning programming that includes writing pseudocode. This method will be used throughout the remaining tasks and projects. Define- Develop- Write the Code.
Discussion of blinking a physical light.
  Physically demonstrate by turning on and off a light switch or a flashlight.
  Instructor model thinking about and writing down the major steps in a program before beginning to write the code.
    For example:
      Step 1: Turn Light On
      Step 2: Wait 1 second
      Step 3: Turn Light Off
      Step 4: Wait 1 second
      Note: In future lessons we will guide the students to write the major program steps themselves.
Students write the code to blink a light. (see calculator details for background on the next slides)
  Note: Let’s use COLOR.RED (or student’s choice among COLOR.RED, COLOR.GREEN and COLOR.BLUE). This is more interesting than LIGHT and gives some options to offer challenges for students who get ahead.
  Discussion the blinking cycle
    Looking at the program, ask the class how many seconds it will take to run the program for 1 blink. If you ran the program over and over, how many blinks would you get in a minute. (Mention in passing that the number of times that something is done in a period of time is called the frequency. The idea of frequency will come up again with programming.)
  Discuss what happens to the blinking if you change the Wait time to be larger or smaller. Instructor make a change, save and run with the class. Have the class predict whether the blink will happen faster or slower before running the program for them. Also, somewhere in the discussion talk about the frequency.
    If the Wait time is 2 seconds, will the blink be faster or slower? How long will it take to complete one blink? How many blinks would there be in a minute?
    Have the students try their own wait times. Ask them to think blink speed, how long one blink will take and how many blinks per minute.
  Note: At some point in the discussion, ask how the blinking LED compares to displaying “Hello World.” What is similar between the two. Is the blinking LED an output or an input? Is displaying “Hello World and output or an input?
  Once you have written one on-off cycle, talk about how you would have the program blink 2 times. Have the students type the pattern again for a second cycle.
    After the students have entered the commands for a second blink and run their program, ask them what they would do if they wanted to do 10 blinks or 100 blinks.
    After discussion of the amount of effort and time to code all the steps so many times, tell them that earlier programmers saw the same problem of entering over-and-over and invented Loops to repeat a set of commands over and over.
    Next time we are going to learn about something called the For loop.

## Slide 26: Student Task: Blink the RGB LED
Example Code
Send("SET COLOR.BLUE ON”)
Wait 2
Send ("SET COLOR.BLUE OFF”)
Wait 2
Student Task: Blink the RGB LED
  Create and execute a program that makes the RGB LED blink multiple times.
TI-84
?
Notes: Example program to turn one of the COLOR options ON and OFF. You could also use COLOR.RED or COLOR.GREEN.
Example program using a For loop to blink an LED 10 times.

## Slide 27: Exploration
How many seconds it will take to run the program for 1 blink? If you ran the program over and over, how many blinks would you get in a minute
What happens to the blinking if you change the Wait time to be larger or smaller?
If the Wait time is 2 seconds, will the blink be faster or slower? How long will it take to complete one blink? How many blinks would there be in a minute?
How long will one blink will take? How many blinks per minute?
How does blinking LED compares to displaying “Hello World.”? What is similar between the two? Is blinking LED an output or an input? Is displaying “Hello World and output or an input?
Notes: . (Mention in passing that the number of times that something is done in a period of time is called the frequency. The idea of frequency will come up again with programming.)

## Slide 28: Extension:
Student Task: Using a For loop, blink the RGB LED for 10 times.
Sample Code:
For(C,1,10)
Send("SET COLOR.BLUE ON”)
Wait 2
Send ("SET COLOR.BLUE OFF”)
Wait 2
End
TI-84
?
Notes: Example program to turn one of the COLOR options ON and OFF. You could also use COLOR.RED or COLOR.GREEN.
Example program using a For loop to blink an LED 10 times.

## Slide 29: Background: Resources for programming and TI-Innovator
10 Minutes of Code with TI-Innovator™ introductory videos on Youtube
  TI-Nspire CX (based on OS version 4.4) https://www.youtube.com/watch?v=anbCjEUAkmQ
TI-Innovator™ introductory video
  https://education.ti.com/en/activities/stem/path-to-stem/nspire-cx#lightbox=ti-innovator-intro-videos
TI-Innovator™ System online Programming eGuides
  https://education.ti.com/html/webhelp/EG_Innovator/EN/index.html

## Slide 30: 3. Mini Project: Using InPut and OutPUT

## Slide 31: Brightness Sensor on TI-Innovator Hub
On-Board Light Brightness Sensor is built into the TI-Innovator Hub. It is located at the bottom of the Hub. The sensor detects light intensity.
Readings range from 0 to 100.

## Slide 32: Example Code- Brightness Sensor
Sample Code:
For (A,1,20)
Send("READ BRIGHTNESS”)
Get(B)
Disp B
Wait 1
End
TI-84
?
Notes: If you need more introductory lesson on the brightness sensor please see Unit 3 of 10 Minutes of Code with TI-Innovator

## Slide 33: Playing a Sound on the TI-Innovator Hub
The speaker built into the TI-Innovator is controlled by the SOUND command. The SOUND command includes a frequency for the sound and a time value to play the frequency. If no time value is provided, the frequency will be played for 1 second.
Sample Code: Send(“SET SOUND frequency TIME seconds”)
Send("SET SOUND 440”)
Wait 1
Send("SET SOUND 261 TIME .5”)
Wait .5
TI-84

## Slide 34: Student Task: Write Program that controls sounds based on light
  Before starting to program, define the problem. Some questions to think about:
  How will the light control sound?
  What sound will the TI-Innovator Hub make?
  How long will the sound play?
  What is your input and what is your output?
Notes: Please see Unit 3 of 10 Minutes of Hub for TI-Innovator Hub for additional support.

## Slide 35: Using a flowchart to plan:
Input
Decision Point
Output
Sample, simple flowchart:
Notes: Flowcharts can be helpful tools to think through what the program needs to do.
More about using Flowcharts for planning:
https://www.codeavengers.com/notes/planning/flowcharts
draw.io is a good online tool you can use to create flowcharts. You can logon with a Google Drive account.

## Slide 36: Student Task: Write Program that controls sounds based on light
2. Develop the Solution: Write down the steps before programming. Use this template:
Important steps in your program | TI-Basic commands to implement steps in your program
1. | 
2. | 
3. | 
4. | 
5… | 

## Slide 37: Student Task: Write Program that displays “low light” or “lots of light” based on the light reading. Play an appropriate sound for each state.
3. Write the code : Follow your pseudocode plan, and assimilate the code snippets to write your program.

## Slide 38: Example Code:
For A,1,20
Send("READ BRIGHTNESS”)
Get(B)
Disp B
If B<50
Then
Disp ”Lots Light”
Send(“SET SOUND 250 TIME 1)
Wait 1
End
Wait 1
End
TI-84

## Slide 39: Exploration
What changes the readings from the values for the brightness sensor?
What does a reading of 0 mean or 50, 100?
Why might you use a Wait command in your For Loop for monitoring the brightness?

## Slide 40: Extension
Student Task:
Add multiple thresholds that trigger different sounds
Instead of using a predetermined frequency, try creating a function for frequency which takes the brightness as a value.
Command Hints:
2->B
While B>1
Send (“Read Brightness”)
Get (B)
Send(“SET SOUND eval(F)”
Wait .2
End
TI-84
Notes: The Full lesson can be found Unit 3: Application 10 Mintutes of Code with TI-Innovator Hub

## Slide 41: Extension:
Student Task: Using a For loop, write a function for frequency which takes the brightness as a value
For(i,1,10)
Send("READ BRIGHTNESS “)
Get(b)
Disp b*600
Send("SET SOUND eval(b*600) TIME 1“)
Wait 1
EndFor
?
TI-84
Notes: Example program to turn one of the COLOR options ON and OFF. You could also use COLOR.RED or COLOR.GREEN.
Example program using a For loop to blink an LED 10 times.

## Slide 42: 4. Introduction to External Input and Output devices

## Slide 43: External Input and Output
Input
  Digital Temperature and Humidity (DHT)
  Light Level
  Soil Moisture
Output
  MOSFET Transistor to control pump
Notes: Discussion how these

## Slide 44: External Input and Output
Input
Output

## Slide 45: Discussion
What are examples of types of Input and Output devices in real life products?
INPUT
OUTPUT
Notes: Possible student responses:
Input  Keyboard, microphone, webcam,
Output  Monitor, printer, projector, headphones

## Slide 46: 4.1 Mini project: using an external light Level sensor
External Input and Output

## Slide 47: Student Task: Create a program that reads input from an external light sensor and then use If-Then-Else logic to control outputs.
  Before starting to program, define the problem. Some questions to think about:
  How will the light control sound?
  What sound will the TI-Innovator Hub make?
  How long will the sound play?
  What is your input and what is your output?
Notes: Please see Unit 3 of 10 Minutes of Hub for TI-Innovator Hub for additional support.

## Slide 48: Using a flowchart to plan:
Create your own flowchart for this project.
Compare your flowchart with another group. What are the similarities and differences?
Adjust your flowchart, if necessary.
Notes: Flowcharts can be helpful tools to think through what the program needs to do.
More about using Flowcharts for planning:
https://www.codeavengers.com/notes/planning/flowcharts

## Slide 49: Light Level Sensor (external)
Light level: relative brightness value in 0-16384 range (2^14, “14 digit resolution”)
Send("CONNECT LIGHTLEVEL 1 TO IN 3 ”)
Send(“RANGE LIGHTLEVEL 1 0 100”)
For(C,1,50)
Send("READ LIGHTLEVEL 1”)
Get(V)
Disp V
Wait 1
End
TI-84
Notes: Technical Notes:
The 0-16384 results can be mapped to 0-100 (if desired) using the RANGE command
Send “RANGE LIGHTLEVEL 1 0 100”

## Slide 50: Student Task: Create a program that reads inputs from an external light sensor and then use If-Then-Else logic to control outputs.
2. Develop the Solution: Write down the steps before programming. Use this template:
Important steps in your program | TI-Basic commands to implement steps in your program
1. | 
2. | 
3. | 
4. | 
5… | 
Notes:   Create a program to connect an external light level sensor, then set up a loop to repeatedly read the light level value, display the light level value, use If-Then(-Else) decision making to determine and set the value of a TI-Innovator physical output (COLOR.BLUE 0-255 or SOUND). If there is time, replace For loop with a While loop.

## Slide 51: Student Task: Create a program that reads inputs from an external light sensor and then use If-Then-Else logic to control outputs.
3. Write the code : Follow your pseudocode plan, and assimilate the code snippets to write your program.

## Slide 52: Things to Consider: Input-Output Control System
Setup
What inputs and outputs need to be connected?
Which ports are they connected to?
Loop to monitor and decide
What loop will you use to repeatedly check the sensors and decide when to set output values? (For, While,…)
Checking the sensor values
What sensors need to be read?
What variables will you “Get” the sensor values to?
Deciding to set new output values
What If-Then or If-Then-Else statements are needed?
What sensor values should be used as decision points in the If statements.
Output (starting, output level(s), stopping)
What output level(s) and patterns do you want to use?
What sensor values or amount of time should cause the output to stop?

## Slide 53: Example Program
Send("CONNECT LIGHTLEVEL 1 TO IN 1 ”)
Send("RANGE LIGHTLEVEL 1 0 100”)
For(c,1,20)
Send "READ LIGHTLEVEL 1”
Get (v)
Disp v
If v<20 Then
Send(“SET SOUND 250 TIME 1)
Wait .5
Else
Send(“SET SOUND 350 TIME 1)
Wait .5
EndIf
EndFor
The CONNECT command is needed to associate the port with a type of device. Each device type has defined properties that the TI-Innovator uses to interpret and communicate electronic signals.
The RANGE command maps the light level reading to a 0 to 100 scale.
TI-84

## Slide 54: Exploration
Some possible challenges/tasks for additional exploration:
  Have the students choose their own colors which are a mix of R,G and B
  Replace or add sound output
  Change the program to map the light level value to the color brightness value (0-255).
  Change the program to map the light level value to a sound frequency.
  Change the program to use a While loop instead of a For loop

## Slide 55: 4.2 Mini project: using Digital Temperature and Humidity Sensor
External Input and Output

## Slide 56: Connecting the Digital Temperature and Humidity Sensor (DHT)
Measurements:
DHT Temperature: temperature in degrees Celsius
DHT Humidity: relative humidity in % (0-100)
The numbering of the temperature sensors helps to differentiate in situations where multiple temperature sensors are connected
Send("CONNECT MOISTURE 1 TO IN 2 ”)
Send(”RANGE MOISTURE 1 0 100”)
Send("READ MOISTURE 1”)
Get(M)
Disp M
**Make sure sketch on the TI-Innovator Hubs are up to date. Blue DHT requires at least v 1.3
TI-84
Notes: **Recommend using port 1 or 2 for the humidity sensor.
Technical Notes:
Blue DHT
Sampling Rate: 1/2 Hz (1 sample per 2 seconds)
Warmup time: ~ 4 seconds (reads -273 C until warmed up)

## Slide 57: Warming up the DHT Sensor:
It might take 4 seconds for the sensor to warm up. How will this influence your code?
Code for “warming up” DHT Sensor
Disp "WARMING UP SENSORS”
−273T
While T<−270
Send("READ DHT 1 TEMPERATURE”)
Get(T)
Wait 1
End
TI-84

## Slide 58: Student Task: Create a program that reads input from an external digital temperature and humidity sensor and then use If-Then-Else logic to control outputs.
  Before starting to program, define the problem. Some questions to think about:
  What are the boundaries for the ideal room temperature?
  What are the boundaries for the ideal room humidity?
  What messages will you display to the screen?
  Will the TI-Innovator Hub make different sounds based on values?
  How long will the sound play?
  What is your input and what is your output?
Notes: Please see Unit 3 of 10 Minutes of Hub for TI-Innovator Hub for additional support.

## Slide 59: Using a flowchart to plan:
Create your own flowchart for this project.
Compare your flowchart with another group. What are the similarities and differences?
Adjust your flowchart, if necessary.
Notes: Flowcharts can be helpful tools to think through what the program needs to do.
More about using Flowcharts for planning:
https://www.codeavengers.com/notes/planning/flowcharts

## Slide 60: Student Task: Create a program that reads input from an external digital temperature and humidity sensor and then use If-Then-Else logic to control outputs.
2. Develop the Solution: Write down the steps before programming. Use this template:
Important steps in your program | TI-Basic commands to implement steps in your program
1. | 
2. | 
3. | 
4. | 
5… | 
Notes:   Create a program to connect an external light level sensor, then set up a loop to repeatedly read the light level value, display the light level value, use If-Then(-Else) decision making to determine and set the value of a TI-Innovator physical output (COLOR.BLUE 0-255 or SOUND). If there is time, replace For loop with a While loop.

## Slide 61: Student Task: Create a program that reads input from an external digital temperature and humidity sensor and then use If-Then-Else logic to control outputs..
3. Write the code : Follow your pseudocode plan, and assimilate the code snippets to write your program.

## Slide 62: 4.3 Mini project: Adding the Soil Moisture Sensor
External Input and Output
Notes: The final step is to layer on the moisture sensor.

## Slide 63: Soil Moisture (external)
Soil Moisture
Sensor
Send("CONNECT MOISTURE 1 TO IN 2 ”)
Send(”RANGE MOISTURE 1 0 100”)
Send("READ MOISTURE 1”)
Get(M)
Disp M
Measurements
Soil Moisture: relative moisture value in 0-16384 range (2^14, “14 digit resolution”)
Technical Notes:
The 0-16384 results can be mapped to 0-100 (if desired)
using the RANGE command
Send “RANGE MOISTURE 1 0 100”
TI-84
Notes: Measurements
Soil Moisture: relative moisture value in 0-16384 range (2^14, “14 digit resolution”)
Technical Notes:
The 0-16384 results can be mapped to 0-100 (if desired)
using the RANGE command
Send “RANGE MOISTURE 1 0 100”

## Slide 64: Student Task: Add the soil moisture sensor to your hub. Open your external temperature and humidity program from the previous task. Add the code to read soil moisture. Once your code is ready, test your program at one of the prepared soil stations.
** Moisture sensor should be handled somewhat delicately as the prongs can/will bend and break:
  Do not force into hard dirt, and
  only the tines of the moisture sensor should come in contact with liquid.
Notes: Option #1: Prep at least three different soil stations each with a different moisture content. Prepare one that is extremely dry that should indicate the soil should be watered to support plant life. Prepare another one that is too moist to indicate overwatered terrain. The last one should be at an “ideal” level for plant growth. These three stations will give students different reference readings for their final Smart Water project. Option #2- next slide has details on outdoor data collection as an option to this.

## Slide 65: Student Task (option 2) : Outside Data Collection Add the soil moisture sensor to your hub. Open your external temperature and humidity program from the previous slides. Add the code to read soil moisture. Once your code is ready, the class will go outside so you can test your sensors. Be careful with the sensors while you test them out.
** Moisture sensor should be handled somewhat delicately as the prongs can/will bend and break:
  Do not force into hard dirt, and
  Only the tines of the moisture sensor should come in contact with liquid.
Notes: Ideally, there should be several places students can test. Students should have readings that indicate the soil is too dry, too wet and ideal for plant growth. Students need to take care when using the soil sensor, if necessary, students might need to pre-dig a small hole with a stick to be able to use the sensor in the soil. Students might also want to use this time to measure the different light levels in sunny and shady locations.

## Slide 66: MOSFET (Field Effect Transistor) and Water Pump Set up and Code
4.4 /Output
Notes: The following slides show introduce the transistor pieces and pump assembly. This will not be done until the final step of the project.

## Slide 67: Pump Control Sub-System Overview
Submersible 3V DC Motor Pump
Note: If connection to MOSFET is reversed then pump flow is reversed.
The system uses a small submersible pump. The pump flow (volume per unit time) is controlled by commands sent from the TI-Basic program through the TI-Innovator to a MOSFET (Field Effect Transistor).
MOSFET (Field Effect Transistor)
Controls the power level to the pump.
Control
MOSFET/ANALOG.OUT: control levels, 0-255 (2^8, 8-bit control)
An external battery source is required to provide enough power to the pump. We can use a 4xAA battery pack.

## Slide 68: Connecting the AA battery pack and MOSFET to pump
Battery Pack negative lead wire (black) to MOSFET (-) terminal
Battery Pack positive lead wire (red) to MOSFET (+) terminal
to pump
MOSFET GND (ground) to Pump (–) lead wire (white)
MOSFET OUT to Pump (+) lead wire (red)
MOSFET to OUT 1
MOSFET OUT to Pump (+) lead wire (red)
MOSFET GND (ground) to Pump (–) lead wire (white)
Battery Pack negative lead wire (black) to MOSFET (-) terminal
Battery Pack positive lead wire (red) to MOSFET (+) terminal
AA Battery Pack

## Slide 69: Pump Control Sub-System – AA Battery Pack
Send("CONNECT ANALOG.OUT 1 TO OUT 1 ”)
255→P
10→N
Send("SET ANALOG.OUT 1 eval(P)”)
Wait 1
Send("SET ANALOG.OUT 1 0”)
MOSFET to OUT 1
MOSFET OUT to Pump (+) lead wire (red)
MOSFET GND (ground) to Pump (–) lead wire (white)
Battery Pack negative lead wire (black) to MOSFET (-) terminal
Battery Pack positive lead wire (red) to MOSFET (+) terminal
AA Battery Pack
TI-84
Notes: The system uses a small submersible pump. The pump flow (volume per unit time) is controlled by commands sent from the TI-Basic program through the TI-Innovator to a MOSFET (Field Effect Transistor).
An external battery source is required to provide enough power to the pump. In the version of the project below we use a 4xAA battery pack and a MOSFET connected to the TI-Innovator to control the pump.

## Slide 70: Making the Pump work: Example Program
Send "CONNECT ANALOG.OUT 1 TO OUT 1”
“ANALOG.OUT 1 is the object that sets the power level of the MOSFET and the speed of the pump. “
For(n,1,5)
Send("SET ANALOG.OUT 1 eval(45*N))”
Wait 3
Send "SET ANALOG.OUT 1 0”
Wait 3
End
The loop pulses the pump in 3 second increments at increasing power levels from the MOSFET starting at level 45 and growing to 225 in steps of 45. The pump stays on during a 3 second waiting period followed by a command to turn the pump off (power level 0).
Student Tasks:
  Let’s practice working with the pump:
    Set-up the MOSFET and pump, according to the previous slides.
    Write the code to turn on the pump for 3 seconds
  Extensions:
    Try the pump at different levels (0-255) (and observe interaction with the soil)
    Try different patterns for pumping the water (trickle, pulse,…)
TI-84

## Slide 71: 5. Putting it all Together- Smart Water Project

## Slide 72: Design Challenge
Design a system that will:
monitor environmental conditions that are relevant to food production agriculture.
control the flow of water from a collection cistern.
incorporate an algorithm in a TI-BASIC program that optimizes the effective delivery of a limited amount of water based on the present environmental conditions.

## Slide 73: Science and Engineering Design Challenge
Make a sketch of a control system that could be used to monitor and meter water from a rain collection cistern that might be used to irrigate a small family garden in Zimbabwe. Include the following:
  Sensors -inputs
  Actuators - outputs
  Control logic - decisions

## Slide 74: Student Task: Create a program that reads input from the temperature, moisture, and light sensors and then use If-Then-Else logic to control the submersible water pump.
  Before starting to program, define the problem. Some questions to think about:
  What are the boundaries for the ideal temperature for watering?
  What are the boundaries for the ideal humidity for watering?
  What re the boundaries for the ideal moisture?
  What messages will you display to the screen?
  How will you control the flow of water?
  How long will it water?

## Slide 75: Science Background:
Students will need to apply concepts from science to understand the system that needs to be controlled. A model of the system is either drawn or written by the student.
Students may find it helpful to complete the following definition sheets to review and/or learn relevant vocabulary.
Refer to the “Teacher Resources” PPT for additional science background info.

## Slide 76: Design: Factors Affecting a Home Garden Ecosystem
Abiotic Factors
Sunlight
Soil grain size and compaction
Soil moisture
Heat
Temperature
Humidity
Soil nutrients
Precipitation
Accumulation
Runoff
Nutrient leeching
Evaporation
Biotic Factors
Photosynthesis
Transpiration
Nutrient uptake
Water uptake
Interactions
Sunlight and primary production
Evaporation/transpiration and humidity
Evaporation/transpiration and temperature
Precipitation and runoff
See NGSS Middle School Life Sciences LS2: Interactions, Energy, and Dynamic Relationships in Ecosystems
http://www.nextgenscience.org/sites/default/files/MS%20LS%20DCI%20combinedf.pdf

## Slide 77: Define factors and interactions
Handout

## Slide 78: Define factors and interactions
Handout

## Slide 79: Using a flowchart to plan:
Create your own flowchart for this project.
Compare your flowchart with another group. What are the similarities and differences?
Adjust your flowchart, if necessary.
Notes: Flowcharts can be helpful tools to think through what the program needs to do.
More about using Flowcharts for planning:
https://www.codeavengers.com/notes/planning/flowcharts

## Slide 80: Student Task: Create a program that reads input from the temperature, moisture, and light sensors and then use If-Then-Else logic to control the submersible water pump.
2. Develop the Solution: Write down the steps before programming. Use this template:
Important steps in your program | TI-Basic commands to implement steps in your program
1. | 
2. | 
3. | 
4. | 
5… | 

## Slide 81: Student Task: Create a program that reads input from the temperature, moisture, and light sensors and then use If-Then-Else logic to control the submersible water pump.
3. Write the code : Follow your pseudocode plan, and assimilate the code snippets to write your program
Final Step: Test, debug, and revise as needed.

## Slide 82: Student Task (Advanced): Create a program that reads input from the temperature, moisture, humidity and light sensors and then use If-Then-Else logic to control the submersible water pump. How could you code your program so it doesn’t water, if it is raining?
3. Write the code : Follow your pseudocode plan, and assimilate the code snippets to write your program
Final Step: Test, debug, and revise as needed.
Notes: This task has them use ALL 4 devices to control the pump. It may be best to have students first try 2 devices, than add a third to the code, then try all 4.

## Slide 83: Assembly of the Pump:
The students will work on the construction of their project. Supplies for building should be made available.
Teams assemble, program, troubleshoot, etc. their solutions.
Teams share their progress and observations.
Teams will likely have to test, retest, and debug until a working pump is achieved.

## Slide 84: Additional tasks to try….
Have the students create the code to determine if the DHT sensor is warmed up or not.
Have the students try simple If-Then-Else statements for determining the best conditions to pump
Have the students create decision statements that incorporate multiple sensors using and and or.
Incorporate light level, moisture, temperature and humidity into the decision to set the pump or not.
Discuss and try different threshold values for the best conditions to pump or not.
Try the pump at different levels (0-255) (and observe interaction with the soil)
Try different patterns for pumping the water (trickle, pulse,…)
Can you restructure the program to use a While loop with a way for you to stop the program instead of a For loop.
Notes: If some students finish earlier than others, this slide can be used to prompt students to try other configurations with their set-up and code….

## Slide 85: Background: Control System

## Slide 86: 6. Presentation: Present and Explain

## Slide 87: Team Presentations:
Have teams host a gallery-walk and encourage peer review of solutions in a less formalized manner.
Or, Have teams prepare presentations to deliver to their classmates
  Teams share their final solutions
  Reflection discussion on the project
Notes: Consider preparing certificates for students for completion of project, especially if it is a summer-time camp scenario.
Consider having students “vote on” the best design and explanation, and offering a small prize.

## Slide 88: Example Program (Basic)
Send("CONNECT LIGHTLEVEL 1 TO IN 1”)
Send("CONNECT DHT 1 TO IN 2”)
Send("CONNECT MOISTURE 1 TO IN 3”)
Send("RANGE LIGHTLEVEL 1 0 100”)
Send("RANGE MOISTURE 1 0 100”)
Disp "WARMING UP SENSORS”
−273T
While T<−270
Send("READ DHT 1 TEMPERATURE”)
Get(T)
Wait 1
End
For n,1,50
Send("READ LIGHTLEVEL 1”)
Get(L)
Send("READ MOISTURE 1”)
Get(M)
Send("READ DHT 1 TEMPERATURE”)
Get(T)
Send("READ DHT 1 HUMIDITY”)
Get(H)
Disp "TEMPERATURE=”,T,"HUMIDITY=”,H,"LIGHT=”,L,"MOISTURE=”,M
Wait 1
If L<50 and M<5
Then
Disp ”GOOD CONDITION TO PUMP”
Send("SET ANALOG.OUT 1 128 TIME 3“)
Else
Disp “NOT A GOOD CONDITION TO PUMP”
End
End
TI-84
Notes: Thresholds will vary based on available light, moisture and humidity. Students will need to observe their values displayed on the screen and change accordingly.

## Slide 89: Example Program (Advanced)
Send("CONNECT LIGHTLEVEL 1 TO IN 1”)
Send("CONNECT DHT 1 TO IN 2”)
Send("CONNECT MOISTURE 1 TO IN 3”)
Send("RANGE LIGHTLEVEL 1 0 100”)
Send("RANGE MOISTURE 1 0 100”)
Disp "WARMING UP SENSORS”
−273T
While T<−270
Send("READ DHT 1 TEMPERATURE”)
Get(T)
Wait 1
End
For n,1,50
Send("READ LIGHTLEVEL 1”)
Get(L)
Send("READ MOISTURE 1”)
Get(M)
Send("READ DHT 1 TEMPERATURE”)
Get(T)
Send("READ DHT 1 HUMIDITY”)
Get(H)
Disp "TEMPERATURE=”,T,"HUMIDITY=”,H,"LIGHT=”,L,"MOISTURE=”,M
Wait 1
If L<50 and M<5 and H > 80
Then
Disp ”Might Rain”
Else
If L<50 and M<5
Then
Disp ”GOOD CONDITION TO PUMP”
Send("SET ANALOG.OUT 1 128 TIME 3“)
Else
Disp “NOT A GOOD CONDITION TO PUMP”
End
End
TI-84
Notes: Thresholds will vary based on available light, moisture and humidity. Students will need to observe their values displayed on the screen and change accordingly.

## Slide 90: Background: Control System

## Slide 91: Background: For loop
Program Editor Control Menu
The For loop repeats a set of commands a specified number of times.
Command Syntax:
For( counter variable,beginning value ,ending value,[step value])
…
End
Notes:
counter variable also known as index variable
The step value is optional, the default step is 1
End is required to close the loop
For(C,1,10)
Disp C
End
For(C,1,50)
Send("READ BRIGHTNESS”)
Get(B)
Disp B
Wait 1
End
This loop will send a command to the TI-Innovator to read the built-in BRIGHTNESS sensor value, it will get the value and store it to variable B and then it will print the value of variable B. The program waits 1 second after the display before proceeding to the end of the loop. This loop repeats 50 times.
This loop will display 1,2,3, … 10.
TI-84

## Slide 92: Background: Decision Making and Logic Statements
If B>10
Then
Disp “B IS GREATER THAN 10”
Send("SET COLOR 0 255 0”)
End
If-Then command
If B>10
Then
Disp “B IS GREATER THAN 10”
Send("SET COLOR 255 0 0”)
Else
Disp “B LESS THAN OR EQUAL TO 10”
Send("SET COLOR 0 0 255”)
End
If-Then-Else command
If B>10 and C>100
Then
Disp “B GREATER THAN 10 AND C GREATER THAN 100”
Send("SET COLOR 0 255 0”)
End
“and”
If B>10 or C>100
Then
Disp "B GREATER THAN 10 OR C GREATER THAN 100”
Send("SET COLOR 0 255 0”)
End
“or”
Logic functions
Decision Making Commands

## Slide 93: Background: While loop
The While loop repeats a set of commands as long as the While condition is true.
Command Syntax:
While condition
Commands in While block
End
1B
While B>0
Send("READ BRIGHTNESS ”)
Get(B)
Disp B
If B>10
Then
Send("SET COLOR.GREEN ON”)
Else
Send("SET COLOR.GREEN OFF”)
End
End
Disp "WHILE LOOP IS COMPLETE"
This While loop is set to continuously ask the TI-Innovator to read the BRIGHTNESS sensor value, gets the value to variable ‘B’, display the value of ‘b’ and then make an If-Then-Else decision to turn on or off a green LED based on the value of ‘B’. The loop can be stopped by a ‘b’ value of zero, which can be achieved by completely covering the sensor. The While loop is able to run the first time because an initial value greater than zero is stored to ‘B’. When the loop stops a message is displayed to inform the user that the loop is complete.

## Slide 94: Background: Storing to numeric and string variables
  You can store to numeric and string variables using the [Sto ] (Store) key:
  String variables, Str1, Str2,…Str0, are found on [vars] menu
2+3→A
Disp A
”BBB”→Str1
Disp Str1
Using Sto 
Example program execution

## Slide 95: Background: Storing TI-Innovator sensor readings to a list
By using the For loop counter variable you can store successive sensor readings into a list for later use.
For (N,1,5)
Send "READ BRIGHTNESS ”
Get(B)
BL1(N)
Wait 1
End
This example stores BRIGHTNESS values to list L1. (N) accesses the nth element of the list.
0.5W
For (N,1,5)
Send "READ BRIGHTNESS ”
Get(B)
(N-1)*WL1(N)
BL2(N)
Wait W
End
This more advanced example estimates the time of the reading by using a variable W, as the time input for the Wait command. The time value is stored into list L1 and the brightness value is stored into L2.